## Slide 1
NVE CORPORATION
Isolators
Pete Eames
Dan Baker
May 07, 2020

## Slide 2
  The IsoLoop four “Bs”:
  Boxes—MSOPs, QSOPs, SOICs, and True 8 mm creepage
  Baud—Highest speed; lowest jitter
  Batteries—Low power consumption
  Bullet-proof—Unlimited barrier life; best isolation voltage; radiation tolerant; low emissions
Slide 2

## Slide 4
Slide 4
Transceiver Demo Board

## Slide 5
Low-Power TMR Isolators (IL29xx / IL01x)
< 0.3 mA/channel typ. Iddq
¼ power of flagship isolators
10 Mbps
RS-485 and data couplers
2.5 kV isolation
NEW!
Slide 5

## Slide 6
Up to 150 Mbps usable baud rate
100 ps jitter
Very low EM emissions and susceptibility
Radiation tolerant
Best isolation voltage (to 6 kVrms)
Polymer/ceramic barrier; 44000-year life
Unique MSOP packages
Unique True 8 (8 mm creepage) packages
IsoLoop Isolator Features (all part families)
Slide 6

## Slide 7
Isoloop Isolator Technology
Aligned
Magnetic Alignment
Opposing
Magnetic Alignment
Aligned electron spins
decreases quantum scattering
Low electrical resistance
Anti-aligned electron spins
increases quantum scattering
High electrical resistance
Spintronics!

## Slide 8
TMR vs. GMR Isolators
Tunneling Magnetoresistance (TMR)
Very large signals
Large resistance for low power
Giant Magnetoresistance (GMR)
Large signals
Low resistance for high speed
10-20 atoms thick
copper
metal-oxide
GMR/TMR Materials Stack
20-30 atoms thick
20-30 atoms thick
magnetic metal
magnetic metals

## Slide 9
Digital and Linear GMR/TMR Films
6/14/19
Field
Digital
Digital material
Latching state
Linear
Proportional material
“Linear” response
  Digital Isolators Materials
  Passive Input Materials
Field
Digital states latched by CMOS
Inherent failsafe
Worlds only monolithic isolator
Magnetically latched outputs
Inherent EMI immunity

## Slide 10
Data
In
Data
Out
Isoloop Isolator
Magnetic
Fields
Input Driver
On-chip Coil
Isolation Barrier
xMR Bridge
Output Driver
Model Signal Path

## Slide 11
Magnetic
Shield
On-chip
Coil
xMR
Resistor
Si Chip with
Active Circuitry
Polymer/ Ceramic
Barrier
Isoloop Isolator Stack-up
Passivation

## Slide 12
Data In+/-
Vdd
Vss
Data Out
Top-Down Die Image
Isolator Chip Construction
Magnetic
Shield
On-chip
Coil
0.2 mm
xMR
Resistors

## Slide 13
Best-in-Class Isolation Barrier
Unique polymer/ceramic composite barrier
Not susceptible to partial discharge, which degrades barrier
Best isolation voltage (to 6 kVrms)
Best Working Voltage (to 1 kVrms)
Highest barrier resistance (1014 Ω)
No aging or diffusion (44000 year barrier life)
Slide 13

## Slide 14
Coming soon
New IL01x low-power TMR isolators
IL700/IL200 high-performance isolators
IL700VE/IL200VE high-voltage isolators
IL400/IL3000 isolated network transceivers
IL500-Series cost-effective isolators
IL600-Series passive-input isolators
New IL600CMTI-Series
IL800-Series top-of-the-line isolators
IL41050-Series Isolated CAN transceivers
IL4600-Series network transceivers + DC-DC
ILDC11 3V-3V DC-DC Converter
IsoLoop Product Families
Slide 14

## Slide 15
IL700/IL200 Series High-Performance Isolators
Slide 15
Low quiescent current (coil is powered only for switching)
3 ns pulse drive
Magnetic latching
Low EMI
High CMTI
1, 2, 4, and 5-channel configurations

## Slide 16
110 Mbps, 3 ns PWD, 100 ps jitter
No clocks or RF carriers for superior EMC
Excellent AC and DC magnetic immunity
Several variants
  IL700-1 Series World’s smallest isolators (MSOP-8; QSOP-16)
  IL700S Series Fastest (150 Mbps); lowest PWD (300 ps)
  IL700T Series Highest operating temperature (125°C)
  IL700V Series Highest isolation voltage (6 kV)
IL700/IL200 Series High-Performance Isolators
Slide 16

## Slide 17
IL700/IL200 Series Key Specifications
Parameter | Min. | Typ. | Max. | Units
Data Rate (S-Series) | 100 (130) | 110 (150) |  | Mbps
PWD (S-Series) |  | 3 (0.3) | 3 | ns
Propagation Delay |  | 10 | 15 | ns
Pulse Jitter |  | 100 |  | ps
Transient Immunity | 30 | 50 |  | kV/µs
Quiescent Current |  | 1.5 | 2 | mA/ch
Temperature Range Std. IL700 Series T-Series IL200 Series | -40 -55 -40 |  | +100 +125 +85 | °C
Slide 17

## Slide 18
IL400 and IL3000 Series Isolated Transceivers
IL422 / IL485
IL3022 / IL3522
IL3122 / IL3185
IL3222 / IL3285
IL3422 / IL3485
IL485W
IL2985 / IL3085 / IL3585 / IL3685
IL41050TA/IL41050TT
IL41050TFD
Slide 18

## Slide 19
RS-422, RS-485, PROFIBUS, and CAN
Digital or passive input versions
Up to 40 Mbps
Rigorous PROFIBUS compliance
True 8 mm creepage available
QSOP and narrow-body versions
Isolated Network Transceivers
Slide 19

## Slide 20
2 Mbps
DC-correct power-up
–40°C to +85°C
MSOP and SOIC packages
IL500 Series Cost-Effective Isolators
Slide 20

## Slide 21
Current-sensitive passive inputs
CMOS or open-drain output
Wide input voltage range
Very high transient immunity
Inherent failsafe output
IL600-Series Passive Input Isolators
Slide 21

## Slide 22
IL600-Series Passive-Input IsoLoop® Isolators
The opto alternative
Slide 22
Analogous to optocoupler but far more reliable
5-8 mA drive current
Very high CMTI
Inherent failsafe output

## Slide 23
IL600CMTI-Series Isolators
NEW!
Ultrahigh CMTI Isolated MOSFET Drivers
200 kV/µs guaranteed CMTI; 300 kV/µs with deglitch
Extended 3 V to 6.6 V power supply range
Switching frequencies up to 50 MHz

## Slide 24
Combine IL700 speed, IL700T temperature, and IL500 DC-correct
110 Mbps
DC-correct power-up
–40°C to +125°C
MSOP, SOIC, and True 8™ packages
IL800 Series Top-of-the Line Isolators
Slide 24

## Slide 25
Isolated Power Devices
Coming May 2020
IL4622
IL4685
ILDC11
World’s smallest DC-DC convertor
3.3 V input to 3.3 V output
Quarter watt output power
Fully-regulated output
Low EMI
Full 2500 V isolation
−40 °C to 125 °C

## Slide 26
Dozens of sensor and isolator boards
Show best practices
Work out of the box
Many are under $100
Evaluation Boards
Slide 26

## Slide 27
Isolator Packages
Exclusive
MSOP
Exclusive
QSOP
transceivers
Slide 27

## Slide 28
Slide 28
VE-Series Ultra-High Voltage Isolators
Notes: Wave 7 is the 7th iteration of our latest push to improve isolators.

## Slide 29
VE-Series Ultra-High Voltage Isolators
Best-in-class high-voltage performance
  6 kVrms isolation
  1 kVrms Working Voltage per VDE V 0884-11
  12.8 kV surge immunity per VDE V 0884-11
  >600 V CTI per IEC 60601
  True 8 mm creepage per IEC 60601
Slide 29

## Slide 30
True 8™ (True 8 mm Creepage) Package
Slide 30

## Slide 31
True 8™ (True 8 mm Creepage) Package
 |  | + | − | =
Package | End Width | Pin-to-end Spacing (total) | Surface Metal Subtraction | Typical Creepage
Ordinary wide-body package | 7.4 mm | 0.7 mm | 0.5 mm | 7.1 mm
NVE True 8™ package | 7.5 mm | 1.0 mm | 0.2 mm | 8.3 mm
Slide 31

## Slide 32
Industrial control (interfaces; networks)
Medical instruments
Energy (smart grids; power supplies)
Automotive (CAN interfaces; battery management systems)
NVE Isolator Markets
Slide 32

## Slide 33
Revolutionary technology
An industry leader
Boxes; Baud; Batteries; Bullet-Proof
Broad product line
Extraordinary support
IsoLoop Isolator Summary
Slide 33

## Slide 34
Isolator New Product Roadmap
= Low power
= Rugged
= Small
Slide 34
3/24/20
1Q 2020 | 2Q 2020 | 3Q 2020
RS485 w/DC-DC Convertor (IL4685E)
3 x 5.5 mm DC-DC Convertor
(ILDC11-15E)
Ultrahigh CMTI Isolators (IL6xxCMTI)
RS422 w/DC-DC Convertor (IL4622E)
Data couplers w/ DC-DC Convertor (IL76xxE)
Solder Bumped Hi Current QFN Regulator
(DC002-90E)

## Slide 35
ISO9001:2015 — Certified UL — Registered VDE — Certified (basic and reinforced insulation) IATF 16949 — Letter of conformance
Isolator Certifications
7/1/19

## Slide 36
Demos and Sample Kits As needed…
Videos nve.com > Videos; www.youtube.com/NveCorporation
Reference Designs www.nve.com/isoapps-reference.php
Competitive Isolator Cross Reference http://www.nve.com/xref/ Competitive Bulletins http://www.nve.com/competition
Distributor/Rep Isolator Support Resources